## Slide 1: Lab 3 Multiplication and Division
CG3207 Group 17

## Slide 2: Improved Unsigned Sequential Multiplier
Check if multiplier[0] is equal to 1 or 0
This will determine if addition of S + A is required
After N cycles, result 2 = MSW of product, result 1 = LSW.

## Slide 3: Trace Unsigned Multiply
This is a trace of an unsigned multiplication using a carry bit (right) and not using a carry bit (left)
As the trace shows, the presence of carry bit concatenate with S and B changes the answer.

## Slide 4: Implementation of Booth’s Algorithm
First check if QR[0] and reg QNPlus1
Depending on answer, either add or subtract, then arithmetic shift right.
Continue cycle until count == width-1 is completed.

## Slide 5: Trace Booth’s Algorithm
*sign extend
The use of sign extend to pad the number of bits of BR and AC is shown that it can lead to a different answer when dealing with the most negative number as multiplicand

## Slide 6: Improvements added
32 bit ALU
The use of Booth Algorithm for Signed Multiplication.
Booth algorithm gives a procedure for multiplying binary integers in signed 2’s complement representation in efficient way.
  Benefits : less number of additions/subtractions required

## Slide 7: Restoring Division
Implemented as per lecture content

## Slide 8: Trace Restoring Division
*carry